## Slide 1: Liebert®
Power Conditioning and Distribution Overview

## Slide 2: power conditioning and distribution products
STS2/PDU (250, 400, 600, 800A)
STS2 (100, 250, 400, 600, 800, 1000A)
FPC (15, 30, 50, 75, 100, 125, 150, 200, 225, 300kVA )
PPC (15, 30, 50, 75, 100, 125, 150, 200, 225, 300, 430, 500, 600, 700, 800kVA)
Liebert PPC
Liebert FPC
Liebert FDC
Liebert RX
Liebert STS2
Liebert STS2/ PDU
4 x 42 Pole Panel Boards
1 x 84 Pole Panel Boards
Transformer Based Distribution Center
Distribution Panel
Static Transfer Switches
In Row
In Room
Legend
Notes: The power distribution and switching portfolio

## Slide 3: Room & Site Based Switching
Liebert STS2 Static Transfer Switch (STS)
  Manual and automatic transfers between two independent AC sources
  Fast, break-before-make switching with 1/4 cycle maximum transfers
Ratings: 100, 250, 400, 600, 800, and 1000 Amp 3-pole designs
Voltages: 208, 220, 240, 380, 400, 415, 480, 600 Volts, 50 or 60 Hz
Front-access only
Top/bottom cable entry
Integral maintenance bypass to both sources
Triple-redundant control logic with optional Liebert Optimized Transfer
Unique Optimized Transfer Capability
Most Reliable with 14 million hours of demonstrated MTBF

## Slide 4: Background
Downstream transformers can cause large saturation current during automatic transfers
Transformer
Saturation
Currents
Trip upstream breakers
Or source failure due to overload

## Slide 5: Transformer Saturation - a Primary Side Switching Problem
Transformer saturation is caused by dc-flux built up during transfers
Can happen especially when the sources are not in phase
Output
Voltages
Xfmr
Fluxes
Output
Currents
DC-Flux
Build up
5x Or Worse Magnetizing Currents

## Slide 6: STS2 Optimized Transfer
Prevents excessive transformer saturation current
Maintains “zero” dc-flux build up during transfers
No
DC-Flux
Build up
Output
Voltages
Xfmr
Fluxes
Output
Currents

## Slide 7: Optimized Transfer Performance Measures
IEEE Benchmark Systems for Static Transfer Switch 2001
Transfer time = time from detection of source failure to transfer completion (full application of the alternate source voltage)
Transfer time, as a performance measure, DOES NOT tell the whole story for the new Optimized STS
Voltages hardly disturbed
Transfer Completed
Output
Voltages
SCR Firing
Signals
Transfer Initiated

## Slide 8: Optimized transfer eliminates concerns of primary side sts
Preferred switch
Alternate switch
Temporary ON pulse
Load Voltage
Alternate Voltage
Transfer reliably up to 180 degrees out of phase
Manage critical load voltage – no disturbance to the load
Control distribution transformer Flux – eliminates surge current
Ensure continuous operation of the critical load
ONLY Liebert STS2 with Optimized Transfer !
Notes: Now we have presented how the static switch improves, reliability, flexibility and utilization: Don’t you think you have a great story for your customers. Now let me tell you about how we absolutely beat the competition,
Why we are the best.
patented technology
One key point from wave form.. Pulse Firing of the alternate source SCR’s to control the transfer and provide a seamless transition from one power source to another.
Secret sauce of static switch.
(Method 1: Phase delay, Method 2: Volt-Second Matching (PDU Transformer Flux management), Method 3: Liebert Wave shaping. Combines operating characteristics of Volt-Second Method for flux management with SCR pulse firing controls to maintain optimum RMS to prevents critical load failures.
Involves mathematical formulations to ensure the following conditions are achieved:
The temporary ON pulse does not cause the flux to move in the wrong direction and cause saturation current to flow
The temporary ON pulse should not result in delaying the occurrence of the final volt-second matching condition

## Slide 9: Room & Site Based Switching & distribution
Liebert STS2/PDU Static Transfer Switch (STS) with PDU
  Secondary Side STS
    The STS is located on the secondary-side (output) of the PDU transformers
  Switching at the 208 volt level of the distribution
Ratings: 250, 400, 600, and 800 Amp
Input Voltage: 480, 600 Volts
Front-Access Only
    Side access for optional distribution
Top and Bottom cable entry
Triple-Redundant Control Logic

## Slide 10: power conditioning and distribution products
STS2/PDU (250, 400, 600, 800A)
STS2 (100, 250, 400, 600, 800, 1000A)
FPC (15, 30, 50, 75, 100, 125, 150, 200, 225, 300kVA )
PPC (15, 30, 50, 75, 100, 125, 150, 200, 225, 300, 430, 500, 600, 700, 800kVA)
Liebert PPC
Liebert FPC
Liebert FDC
Liebert RX
Liebert STS2
Liebert STS2/ PDU
4 x 42 Pole Panel Boards
1 x 84 Pole Panel Boards
Transformer Based Distribution Center
Distribution Panel
Static Transfer Switches
In Row
In Room
Legend
Notes: The power distribution and switching portfolio

## Slide 11: Trends: single stage power distribution?
PDU 1B
PDU 1A
AIR
AIR
PDU 2B
PDU 2A
Heavy Cable
Congestion Underfloor
IT
Rack
IT
Rack
IT
Rack
IT
Rack
Single stage distribution with panelboards located at the PDU, and typical for sizes less than 225kVA

## Slide 12: Trends: two stage power distribution?
Reduces cable congestion and opens up space for more servers
Large data centers
Trend is from single to two stage distribution
PPC/ Outside Room
PPC/ Outside Room
IT
Rack
IT
Rack
IT
Rack
IT
Rack
AIR
AIR
PPC/PDU A
PPC/PDU B
RX
RX
RX
RX

## Slide 13: Room & Site Based Power Distribution Unit
Liebert PPC2 Power Distribution Unit (PDU)
More amps and more poles
  Transformer-based design
Input voltages: 208, 240, 480, 600 Volts
Output voltages: 208/120, 240/139, and 415/240 volts
Packaged power conditioning and distribution
Provides customization options to meet application requirements
Highly efficient with DOE TP-1 transformer design
K – rated transformers available
Ratings: 15, 30, 50, 75, 100, 125, 150, 200, 225, 300, 430, 500, 600, 700 and 800 kVA

## Slide 14: PPC2 150-225kVA - 44” frame Bottom Exit
72 pole SqD
54 pole SqD
Main Input Breaker
Subfeed Breaker
(output)
Panelboard Main Breaker
Main Input Breaker
Panelboard Main Breaker
Notes: The second generation PPC can be broken down in to two functional segments. The first is 15 – 225kVA Rated units with panel board and sub feed distribution. Available with 42, 54, 72 or 84 pole panel board options. Dimensions (

## Slide 15: PPC-SL = a new Design
Design Elements
  Smaller footprint
    62”W x 45”D
  Isolated panelboards and/or subfeed breakers
  Front access only
  Bottom entry/exit
  Identical monitoring options as PPC
  Available kVA ratings
    300 kVA
    430 kVA
    500 kVA
  400 – 600V input
  208/120V output

## Slide 16: PPC SL 500KVA dimensions

## Slide 17: Row Based Power Distribution Unit
Liebert FPC Power Distribution Unit (PDU)
  Transformer-based design
  Row-Based “IT-Cabinet” design that can also be room based (*2 rack size)
2 x 42 pole in-line panel boards standard
Up to 4 x 42 pole panel boards in wide cabinet
Input Voltages: 208, 240, 480, 600 Volts
Output Voltages: 208/120, 240/139, and 415/240 Volts
Bottom and top cable entry/exit
Highly efficient with DOE TP-1 transformer design
Ratings: 15, 30, 50, 75, 100, 125, 150*, 200*, 225*, and 300* kVA

## Slide 18: Liebert FPC
Main Input Breaker
Subfeed Breakers
PMP
Transformer

## Slide 19: power conditioning and distribution products
STS2/PDU (250, 400, 600, 800A)
STS2 (100, 250, 400, 600, 800, 1000A)
FPC (15, 30, 50, 75, 100, 125, 150, 200, 225, 300kVA )
PPC (15, 30, 50, 75, 100, 125, 150, 200, 225, 300, 430, 500, 600, 700, 800kVA)
Liebert PPC
Liebert FPC
Liebert FDC
Liebert RX
Liebert STS2
Liebert STS2/ PDU
4 x 42 Pole Panel Boards
1 x 84 Pole Panel Boards
Transformer Based Distribution Center
Distribution Panel
Static Transfer Switches
In Row
In Room
Legend
Notes: The power distribution and switching portfolio

## Slide 20: Row Based remote power panels
Liebert FDC Remote Power Panel (RPP)
  Transformer-less design
  Row-Based “IT-Cabinet” design that can also be room based
  19” width (One Rack Space)
One, two, or four inputs
Input/output voltages: 208Y/120, 220Y/127, 240Y/139, 380Y/220, 400Y/230, 415Y/240 volts
Four (4) 42-pole panel-boards with individual main breakers (168 poles)
Bottom cable entry/exit design standard
Front and rear access only

## Slide 21: Fdc Benefits
Fills need for more branch circuits
Reduce risks associated with adding circuits
Distribution that
    Is closer to the load
    Is scalable
    Conserves Data Center space
    Is easy to install
    Matches an IT cabinet rack line-up
Top or thru-side cabling capability
Integrated end-to-end power and distribution solution

## Slide 22: FDC details
Power Distribution
Same size as a 19” rack
  23.5”Wx38”Dx77”H
208/120V Input/output voltages
One, two, or four inputs
4 panel-boards with individual main breakers
Front and rear access only
Bottom exit standard
Monitoring options available

## Slide 23: Fdc Top or Side Exit Cable Option
Cables
Cables
Cables

## Slide 24: Introducing the Liebert RX
Delivering Kilowatts for Today's Servers at the Best Cost
400A, 100% rated panelboard mains
Square D 400A, 84 pole, 100% rated panelboard
  Accommodates breakers from 15A 1-phase to 100A 3-phase
30 & 60A branches coordinates well with 100% rated 400 amp mains
22kAIC fault current
Frameless design for max gutter space for wire access and cooling
Meets OSHA required for total separation from energized second source
Optional panelboard main breaker or individual branch circuit metering
Top and bottom entry/exit
1, 2, 3 and 4 unit configurations
  Free standing or wall mountable
Two units mounted back-to-back drop-in floor tile replacement version

## Slide 25: Specifications
Size - 23.75”W x 12” D x 79”H
208/120V Input/output voltage
One input
Top and bottom entry/exit
400A, 100% rated main breaker and panelboard
No panelboard main breaker option
  Not needed with a single input
  Eliminates breaker coordination issues
Hinged interior accent panel
Enclosure
  Sold removable door
  Front access
Metering Options
  CPM – total current, volts, THD, etc
  LDMF – individual branch, V, A ,THD, etc
    100 amp CT strips

## Slide 26: Interior photos

## Slide 27: Panelboard options
Square D 400A, 208V, 22 kAIC rated 84 pole panelboard
ABB 400A, 208V finger-safe 84 pole panelboard
ABB
Square D

## Slide 28: Configuration options
Single – 24”W x 12”D
  Wall mounted
  Back supported by column, Unistrut, Wire cage
  Can not be free standing
Double - Side-by-side – 48”W x 24”D
Wall mounted
Back supported by column, Unistrut, Wire cage
Can not be free standing
Double – Back-to-back 24”W x 24”D
Free standing
Drop-in replacement for floor tile

## Slide 29: Configuration options
Free Standing – 36”W x 24”D
3 units - front, rear and one side
Free Standing– 48”W x 24”D
4 units - front, rear and both sides
Units are shipped unattached (3 per pallet)
Can be bolted together in the field by the customer to make any of the above configurations
Hardware to attach units together is supplied with each unit
Hardware to attach unit to wall or other support is supplied by others.

## Slide 30: All products – monitoring capability SUMMARY
Basic Monitoring
  Power Monitoring Panel (VPMP)
    PDU Input/Output Level
Enhanced Monitoring Options
  Current Plus Monitoring (CPM)
    Panel Board Mains
  Liebert Distribution Monitoring (LDMF)
    CPM + Branch Circuit level monitoring
Monitoring | VPMP | CPM | VPMP+CPM | LDMF | VPMP+LDMF
Input voltage |  |  |  |  | 
Output voltage |  |  |  |  | 
Output current – total |  |  |  |  | 
Output current – each PB |  |  |  |  | 
Output current – each branch circuit |  |  |  |  | 

## Slide 31: Current Plus Monitoring details
Monitors Panelboard Main Breaker
What is Monitored?
    Phase, Neutral and Ground Current
    Percent Load, Power Factor and Crest Factor
    kVA, kW, kW-Hours
    Voltage - Line-to-line and Line-to-neutral
    Voltage and Total Current Harmonic Distortion (THD)
Alarms
    Over and Under Voltage
    Phase Over Current Warning
    Phase Over Current Alarm
    Neutral Over Current Alarm
    Ground Over Current Alarm
    Summary Alarm
Communications
    IntelliSlot Unity Card
    WEB/SNMP, Modbus 485, Modbus over IP, BACNet

## Slide 32: Liebert Distribution Monitoring (LDMF) details
Reports the current level of branch breakers and panelboard main breaker
Panelboard monitoring consist of
    Two current sensor modules
    Each modules has 21 CT to monitor 21 branch breakers
Monitoring
    Phase, Neutral and Ground Current
    Percent Load, Power Factor and Crest Factor
    kVA, kW, kW-Hours
    Voltage - Line-to-line and Line-to-neutral
    Voltage and Total Current Harmonic Distortion (THD)
Alarms
    Over Current Warning
    Over Current Alarm
    Low Current Alarm
Communications
    IntelliSlot Unity Card
    WEB/SNMP, Modbus 485, Modbus over IP, BACNet
100 amp CT strip

## Slide 33: Communication & Interface Cards
UNITY Card
  Supports two simultaneous 3rd party protocols
    SNMP
    Modbus TCP or RTU (485)
    BACNet IP or MSTP (485)
  Email Notifications
  SMS Text Messages
  HTTP Browser
  LIFETM Services
  SN Series sensor support
    Daisy chain up to 10 together
    Temperature
    Temperature/Humidity
    Contact Closure
    Leak Detection